# Government Notice No 45 of 2003

## THE ENVIRONMENT PROTECTION ACT 2002

Regulations made by the Minister under sections 39 and 96

of the Environment Protection Act 2002

1.	These regulations may be cited as the Environment Protection (Standards for effluent discharge into the ocean) Regulations 2003.

2.	In these regulations-

“effluent” means water sullied or contaminated by any matter, in solution or suspension and derived from the use of the water in connection with domestic, industrial or other activities.

“HWM” means the High Water Mark at spring tide;

“lagoon” means the extent of sea from the HWM to the reef barrier;

“ocean” means the large expanse of sea from the HWM in the absence of a reef barrier or from a reef barrier where it exists.

- No person shall discharge, or cause to be discharged effluent into the ocean –

  - unless it complies with the standards prescribed in the Schedule;

  - at a distance less than 300 metres off the reef barrier and at a depth of less than 30 metres where there is a lagoon; or

(c)	at a distance less than 500 metres from the HWM and at a depth of less than 25 metres where there is no lagoon.

4.	Notwithstanding regulations 3, no person shall discharge any effluent into the ocean at a point where sea currents will cause effluent to be taken back into the lagoon.

5.	These regulations shall come into operation on 01 September 2003.

Made by the Minister on 05 February 2003.

SCHEDULE

(regulation 3)

The following standards are permissible limits or range for the corresponding parameters:

| Parameter | Unit | Permissible limits |
| --- | --- | --- |
| Temperature pH Floatables | oC - mm | 40 5 – 9 6 |
| Biochemical Oxygen Demand (BOD5) Chemical Oxygen Demand (COD) Suspended Solids | mg/l mg/l mg/l | 250 750 300 |
| Cadmium Chromium (VI) Chromium, Total Cyanides (as CN-) Lead Nickel Zinc Total Mercury Arsenic | μg/l μg/l μg/l μg/l mg/l mg/l mg/l μg/l μg/l | 20 100 500 100 2 2 2 10 200 |
| Total pesticides Oil & Grease | mg/l mg/l | 1 20 |