# Government Notice No 188 of 1998

MINISTRY OF LOCAL GOVERNMENT &

ENVIRONMENT

##### Guidelines for  Inland Surface Water  Quality

- The following guidelines are hereunder published for the information of the public with the objective of preserving the quality of the inland surface waters for sustaining aquatic life.

- Inland surface water –

- includes water of river, watercourse, stream, lake, pond, dam or reservoir;

- excludes –

- all ground water,

- water contained in any sewer, sewage disposal works, private drain or private reservoir used for irrigation purposes,

- water in any privately owned chamber, tanks or other container, and,

- sea water.

- The public is requested to assist in the preservation of the quality of the inland surface water for the benefit of the community at large.

- For the benefits of those concerned the under mentioned parameters could be adhered to.

## Parameters  	Maximum Limits	Remarks

- Inorganics

Boron..............           	0.75 µg/1

Cadmium ....................  	0.70 µg/1

Chlorine Residual ..........   	2.0  µg/1

Chromium (total) ...........   	2.0  µg/1

Copper .....................   	6.5  µg/1

Cyanide.....................   	5.2  µg/1

Dissolved oxygen (lower limit) 	6.0  mg/1 		(at 25o  C)

Iron ......................... 	1.0  mg/1

Lead ......................... 	1.3  µg/1

Mercury ...................... 	0.1  µg/1

Methyl mercury compounds     	0.012 µg/1

Nickel ....................... 	87.6 µg/1

pH  ......................... 	6.5 - 9.0

Selenium ..................... 	1.0  µg/1

Silver ....................... 	1.2  µg/1

Zinc ......................... 	59   µg/1

Sulphide (H2 S).................. 	2.0  µg/1

Phosphate .................... 	25   µg/1  	for a lake

50   µg/1 	for streams entering a lake

100  µg/1	for streams not entering a lake

(b)  Organics

Dieldrin ...................	0.0019 µg/1

Chlordane  .................	0.0043 µg/1

Pentachlorophenol            	3.5 - 9.5 µg/1 	for pH 6.5 - 7.5

DDT ........................ 	0.001 µg/1

Endosulfan ................. 	0.056 µg/1       	alpha and beta forms

Endrin ..................... 	0.0023 µg/1

Guthion  ................... 	0.01   µg/1

Lindane  ...................	0.08   µg/1

Oil and Greases ........ 	undetectable

PCBs .......................	0.014  µg/1

Suspended solids............ 	10 mg/1 	at background

concentration <100 mg/l

10% of back-       when background

ground conc.	  concentration > 100 mg/l

(mg/1)

Ministry of Local Government

& Environment

23 January 1998